## Slide 1: Conditional Branching (beq)
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
beq $s0, $s1, target # branch is taken
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target: # label
add $s1, $s1, $s0 # $s1 = 4 + 4 = 8
Labels indicate instruction locations in a program. They cannot use reserved words and must be followed by a colon (:).

## Slide 2: The Branch Not Taken (bne)
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
bne $s0, $s1, target # branch not taken
addi $s1, $s1, 1 # $s1 = 4 + 1 = 5
sub $s1, $s1, $s0 # $s1 = 5 – 4 = 1
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5

## Slide 3: Unconditional Branching / Jumping (j)
# MIPS assembly
addi $s0, $0, 4 # $s0 = 4
addi $s1, $0, 1 # $s1 = 1
j target # jump to target
sra $s1, $s1, 2 # not executed
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5

## Slide 4: Unconditional Branching (jr)
# MIPS assembly
0x00002000 addi $s0, $0, 0x2010
0x00002004 jr $s0 #jump to address that is stored in $s0
0x00002008 addi $s1, $0, 1
0x0000200C sra $s1, $s1, 2
0x00002010 lw $s3, 44($s1)

## Slide 5: High-Level Code Constructs
if statements
if/else statements
while loops
for loops

## Slide 6: If Statement
High-level code
if (i == j)
f = g + h;
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j

## Slide 7: If Statement
High-level code
if (i == j)
f = g + h;
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
L1: sub $s0, $s0, $s3
Notice that the assembly tests for the opposite case (i != j) than the test in the high-level code (i == j).

## Slide 8: If / Else Statement
High-level code
if (i == j)
f = g + h;
else
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j

## Slide 9: If / Else Statement
High-level code
if (i == j)
f = g + h;
else
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
j done
L1: sub $s0, $s0, $s3
done:

## Slide 10: While Loops
High-level code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
MIPS assembly code
# $s0 = pow, $s1 = x
addi $s0, $0, 1
add $s1, $0, $0
addi $t0, $0, 128
while: beq $s0, $t0, done
sll $s0, $s0, 1
addi $s1, $s1, 1
j while
done:
Notice that the assembly tests for the opposite case (pow == 128) than the test in the high-level code (pow != 128).

## Slide 11: For Loops
The general form of a for loop is:
for (initialization; condition; loop operation)
loop body
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
loop body: executes each time the condition is met

## Slide 12: For Loops
High-level code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
add $s0, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
Notice that the assembly tests for the opposite case (i == 128) than the test in the high-level code (i != 10).

## Slide 13: Less Than Comparisons
High-level code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
addi $s0, $0, 1
addi $t0, $0, 101
loop: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
sll $s0, $s0, 1
j loop
done:
#$t1 = 1 if i < 101.

## Slide 14: Arrays
Useful for accessing large amounts of similar data
Array element: accessed by index
Array size: number of elements in the array

## Slide 15: Arrays
5-element array
Base address = 0x12348000 (address of the first array element, array[0])
First step in accessing an array: load base address into a register

## Slide 16: Arrays
// high-level code
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
# MIPS assembly code
# array base address = $s0
lui $s0, 0x1234 # put 0x1234 in upper half of $S0
ori $s0, $s0, 0x8000 # put 0x8000 in lower half of $s0
lw $t1, 0($s0) # $t1 = array[0]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 0($s0) # array[0] = $t1
lw $t1, 4($s0) # $t1 = array[1]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 4($s0) # array[1] = $t1

## Slide 17: Arrays Using For Loops
// high-level code
int array[1000];
int i;
for (i=0; i < 1000; i = i + 1)
array[i] = array[i] * 8;
# MIPS assembly code
# $s0 = array base address, $s1 = i

## Slide 18: Arrays Using For Loops
# MIPS assembly code
# $s0 = array base address, $s1 = i
# initialization code
lui $s0, 0x23B8 # $s0 = 0x23B80000
ori $s0, $s0, 0xF000 # $s0 = 0x23B8F000
addi $s1, $0, 0 # i = 0
addi $t2, $0, 1000 # $t2 = 1000
loop:
slt $t0, $s1, $t2 # i < 1000?
beq $t0, $0, done # if not then done
sll $t0, $s1, 2 # $t0 = i * 4 (byte offset)
add $t0, $t0, $s0 # address of array[i]
lw $t1, 0($t0) # $t1 = array[i]
sll $t1, $t1, 3 # $t1 = array[i] * 8
sw $t1, 0($t0) # array[i] = array[i] * 8
addi $s1, $s1, 1 # i = i + 1
j loop # repeat
done:

## Slide 19: ASCII Codes
American Standard Code for Information Interchange
  assigns each text character a unique byte value
For example, S = 0x53, a = 0x61, A = 0x41
Lower-case and upper-case letters differ by 0x20 (32).

## Slide 20: Cast of Characters