## Slide 1: MIPS Assembly with MARS

## Slide 3: First Instructions and execution of an Assembly
Simple program to compute 7+9
Inorder to perform this operation, we need to initialize two registers with these values, and perform addition with add instruction.

## Slide 4: I-Type
Immediate-type
3 operands:
  rs, rt: register operands
  imm: 16-bit two’s complement immediate
Other fields:
  op: the opcode
  Simplicity favors regularity: all instructions have opcode
  Operation is completely determined by the opcode

## Slide 6
How to initialize registers:
$0 register is a special register that contains 0(zero) all the time. You can not change its content.
Add Immediate
addi Rt, Rs, Imm # RF[Rt] = RF[Rs] + Imm
Add contents o f Reg.File [Rs] t o sign extended (se) Imm value; store result in Reg.File[Rt] . If overflow occurs in the two's complement number system, an exception is generated.
Imm is the value to be stored in Rt register
Ex: addi $3,$0,7

## Slide 7: addi $3,$0,7
Code in Hex
0x20030007
2 0 0 3 0 0 0 7
‭0010 0000 0000 0011 0000 0000 0000 0111‬
‭
001000 00000 00011 0000000000000111
OpCode rs rt 16-bit Immediate 2’sc value

## Slide 8: addi $4,$0,9
0x20040009
‭0010 0000 0000 0100 0000 0000 0000 1001‬ (group of 4 bits)
Re-group bits based on following format
001000 00000 00100 0000000000001001

## Slide 10: add $5,$3,$4
Format:ADD rd, rs, rt
0x00642820
‭0000 0000 0110 0100 0010 1000 0010 0000‬
000000 00011 00100 00101 00000 100000‬

## Slide 11: Assembly to machine code translation
Translation into machine code (for simple programs can be done by users) is done by a special program called ASSEMBLER that traslates the Mnemonic program into machine code.
Assembly code | Machine Code | Explanation
addi $3,$0,7 | 0x20030007 | 
addi $4,$0,9 | 0x20040009 | 
add $5,$3,$4 | 0x00642820 | 
This program compiled can converted into machine code that that is 3 32 bit values. These codes will be loaded into memory.
0x20030007
0x20040009
0x00642820
Machine code for performing 7+9

## Slide 12: MIPS Programming Model a representative simple RISC machine
Processor State (inside the CPU)
Main Memory
Fetch/Execute loop:
fetch Mem[PC]
PC = PC + 4†
execute fetched instruction (may change PC!)
repeat!
†MIPS uses byte memory addresses. However, each instruction is 32-bits wide, and *must* be aligned on a multiple of 4 (word) address. Each word contains four 8-bit bytes. Addresses of consecutive instructions (words) differ by 4.
00
PC
r0
r1
r2
...
r31
000000....0
32 bit “words”
0
1
2
3
(4 bytes)
32 bit “words”
0
31
next instruction
General Registers:
A small scratchpad of frequently used or temporary variables
0 4
8
16 20
Addresses
0x20030007
0x20040009
0x00642820

## Slide 13
To execute the program the PC is loaded with the addres of the first instruction of the program. In MARS simulator this is
0x00 40 00 00
At the next fetch cycle, the first instruction (0x20030007
) is brought into CPU (particularly Instruction Register) instruction is decoded and execution of this instruction is performed.
Content
0x20030007
0x20040009
0x00642820
Memory
0x00400000
0x00400004
0x00400008

## Slide 16: The Power of the Stored Program
32-bit instructions and data stored in memory
Sequence of instructions: only difference between two applications (for example, a text editor and a video game)
To run a new program:
  No rewiring required
  Simply store new program in memory
The processor hardware executes the program:
  fetches (reads) the instructions from memory in sequence
  performs the specified operation
The program counter (PC) keeps track of the current instruction
In MIPS, programs typically start at memory address 0x00400000

## Slide 17: Interpreting Machine Language Code
Start with opcode
Opcode tells how to parse the remaining bits
If opcode is all 0’s
  R-type instruction
  Function bits tell what instruction it is
Otherwise
  opcode tells what instruction it is

## Slide 18: Logical Instruction Examples

## Slide 19: Logical Instruction Examples

## Slide 20: Logical Instruction Examples

## Slide 21: Logical Instruction Examples

## Slide 22: Shift Instructions
sll: shift left logical
  Example: sll $t0, $t1, 5 # $t0 <= $t1 << 5
srl: shift right logical
  Example: srl $t0, $t1, 5 # $t0 <= $t1 >> 5
sra: shift right arithmetic
  Example: sra $t0, $t1, 5 # $t0 <= $t1 >>> 5
Variable shift instructions:
sllv: shift left logical variable
  Example: sllv $t0, $t1, $t2 # $t0 <= $t1 << $t2
srlv: shift right logical variable
  Example: srlv $t0, $t1, $t2 # $t0 <= $t1 >> $t2
srav: shift right arithmetic variable
  Example: srav $t0, $t1, $t2 # $t0 <= $t1 >>> $t2

## Slide 23: Shift Instructions

## Slide 24: Generating Constants
16-bit constants using addi:
32-bit constants using load upper immediate (lui) and ori:
(lui loads the 16-bit immediate into the upper half of the register and sets the lower half to 0.)
High-level code
int a = 0xFEDC8765;
MIPS assembly code
# $s0 = a
lui $s0, 0xFEDC
ori $s0, $s0, 0x8765
High-level code
// int is a 32-bit signed word
int a = 0x4f3c;
MIPS assembly code
# $s0 = a
addi $s0, $0, 0x4f3c

## Slide 25: Memory Access Instructions
How to copy data from memory into registers, and how to copy data to memory from registers.

## Slide 26: Load and Store instructions
The MIPS architecture is a Load/Store architecture, which means that the only instructions that access main memory are the load and store instructions. Only one addressing mode is implemented in the hardware.

## Slide 27: Load and Store
The operands for all arithmetic and logic operations are contained in registers.
To operate on data in main memory, the data is first copied into registers.
  A load operation copies data from main memory into a register.
  A store operation copies data from a register into main memory .
When a word (4 bytes) is loaded or stored the memory address must be a multiple of four. This is called an alignment restriction.
Addresses that are a multiple of four are called word aligned. This restriction makes the hardware simpler and faster.

## Slide 28: word aligned
How can you multiply by four in binary? By shifting left 2 positions. Therefore a multiple of 4 looks like some N shifted left two positions. So the low order two bits of a multiple of 4 are both 0.
0x000AE430 Yes.
0x00014432 No.
0x000B0737 No.
0x0E0D8844 Yes.

## Slide 29: lw and sw instructions
The lw instruction loads a word into a register from memory.
The sw instruction stores a word from a register into memory.
Each instruction specifies a register and a memory address.

## Slide 30: MIPS Addresses
The MIPS instruction that loads a word into a register is the lw instruction.
The store word instruction is sw.
Each must specify a register and a memory address.
A MIPS instruction is 32 bits (always). A MIPS memory address is 32 bits (always). How can a load or store instruction specify an address that is the same size as itself?
An instruction that refers to memory uses a base register and an offset(ordisplacement). The base register is a general purpose register that contains a 32-bit address. The offset is a 16-bit signed integer contained in the instruction. The sum of the address in the base register with the (sign-extended) offset forms the memory address.

## Slide 31: Example
Load word instruction in assembly language:
lw $d,off($b) # $d <-- Word from memory address b+off
# $b is a register. off is 16-bit two's complement.
# (The data from memory is available in $d after
# a one machine cycle delay.)
At execution time two things happen:
  an address is calculated by adding the base register b with the offset off, and
  data is fetched from memory at that address.
The base address is always the content of one of the registers in the register file. The displacement is always a 16-bit constant. The constant value can range from - 32,768 (-2^16 ) to + 32,764 ( (2^16) - 4 )

## Slide 32: Example
Following example the instruction loads the word at address 0x00400060 into register $6.
Assume that register $7 contains 0x00400000.
0x00400060 --- address of data
0x00400000 --- address in $10
$8 --- destination register
The instruction is:
lw $6,0x60($7) # $6<--------Memory[0x60+$7]

## Slide 33: store word instruction
sw $s1, 12( $a0 )
When the hardware executes this instruction it will compute the effective address of the destination memory location by adding together the contents of register $a0 and the constant value 12
Mem [ $a0 + 12] <- $s1
A copy of the contents of register $s1 is stored in memory at the effective address.

## Slide 34
Consider given registers $12 and $13 and memory.
Write the instruction that puts the word 0xFFFFFFFF into memory location 0x0004000C.
Register $12 contains 0xFFFFFFFF
Register $13 contains 0x00040014
sw $12 , 0xFFF8($13) or sw $12 , -8($13)
Memory | Addresses
00000005 | 00040014
00000004 | 00040010
00000003 | 0004000C
00000002 | 00040008
00000001 | 00040004
00000000 | 00040000

## Slide 35: How to initialize the Base Register(32-bits)
By using a 32-bit base register and an offset a 32-bit lw or sw instruction can reference all of memory.
But how does the base address get into the base register?
This is where the lui (load upper immediate) instruction is useful.
It copies its 16-bit immediate operand to the upper two bytes of the designated register.
lui $d,const # upper two bytes of $d <— two byte const
# lower two bytes of $d <— 0x0000

## Slide 36
For example, say that memory is as in the picture, and that you want to load the word at 0x00040010 into $12. The lui instruction can set up the base register:
lui $13, 0x0004
lw $12, 0x10($13)
After the lui instruction $13 contains 0x00040000. To get to the address we need, use an offset of 0x10.
Memory | Addresses
00000005 | 00040014
00000004 | 00040010
00000003 | 0004000C
00000002 | 00040008
00000001 | 00040004
00000000 | 00040000

## Slide 37: Filling in the bottom Half
By using the lui instruction, the base register can be loaded with multiples of 0x00010000.
But often you want a more specific address in the base register. Use the ori instruction to fill the bottom 16 bits.
ori $d,$s,imm
zero-extends imm to 32 bits then does a bitwise OR of that with the contents of register $s. The result goes into register $d.

## Slide 38
The lw instruction (below) loads the word at 0x0060500C into $12.
lui $13, 0x0060
ori $13, $13, 0x5000
lw $12, 0xC($13)
The above ori instruction "fills in" the lower 16 bits of register $13 by doing the following:
$13 after lui : 0000 0000 0110 0000 0000 0000 0000 0000
zero-extended imm. op. : 0000 0000 0000 0000 0101 0000 0000 0000
result of bitwise OR : 0000 0000 0110 0000 0101 0000 0000 0000

## Slide 39: Multiplication, Division
Special registers: lo, hi
32 × 32 multiplication, 64 bit result
  mult $s0, $s1
  Result in {hi, lo}
32-bit division, 32-bit quotient, 32-bit remainder
  div $s0, $s1
  Quotient in lo
  Remainder in hi
Moves from lo/hi special registers
  mflo $s2
  mfhi $s3

## Slide 40: Branching
Allows a program to execute instructions out of sequence.
Types of branches:
  Conditional branches
    branch if equal (beq)
    branch if not equal (bne)
  Unconditional branches
    jump (j)
    jump register (jr)
    jump and link (jal)

## Slide 41: Review: The Stored Program

## Slide 42: Conditional Branching (beq)
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
beq $s0, $s1, target # branch is taken
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target: # label
add $s1, $s1, $s0 # $s1 = 4 + 4 = 8
Labels indicate instruction locations in a program. They cannot use reserved words and must be followed by a colon (:).

## Slide 43: The Branch Not Taken (bne)
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
bne $s0, $s1, target # branch not taken
addi $s1, $s1, 1 # $s1 = 4 + 1 = 5
sub $s1, $s1, $s0 # $s1 = 5 – 4 = 1
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5

## Slide 44: Unconditional Branching / Jumping (j)
# MIPS assembly
addi $s0, $0, 4 # $s0 = 4
addi $s1, $0, 1 # $s1 = 1
j target # jump to target
sra $s1, $s1, 2 # not executed
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5

## Slide 45: Unconditional Branching (jr)
# MIPS assembly
0x00002000 addi $s0, $0, 0x2010
0x00002004 jr $s0
0x00002008 addi $s1, $0, 1
0x0000200C sra $s1, $s1, 2
0x00002010 lw $s3, 44($s1)

## Slide 46: High-Level Code Constructs
if statements
if/else statements
while loops
for loops

## Slide 47: If Statement
High-level code
if (i == j)
f = g + h;
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j

## Slide 48: If Statement
High-level code
if (i == j)
f = g + h;
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
L1: sub $s0, $s0, $s3
Notice that the assembly tests for the opposite case (i != j) than the test in the high-level code (i == j).

## Slide 49: If / Else Statement
High-level code
if (i == j)
f = g + h;
else
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j

## Slide 50: If / Else Statement
High-level code
if (i == j)
f = g + h;
else
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
j done
L1: sub $s0, $s0, $s3
done:

## Slide 51: While Loops
High-level code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
MIPS assembly code
# $s0 = pow, $s1 = x
addi $s0, $0, 1
add $s1, $0, $0
addi $t0, $0, 128
while: beq $s0, $t0, done
sll $s0, $s0, 1
addi $s1, $s1, 1
j while
done:
Notice that the assembly tests for the opposite case (pow == 128) than the test in the high-level code (pow != 128).

## Slide 52: For Loops
The general form of a for loop is:
for (initialization; condition; loop operation)
loop body
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
loop body: executes each time the condition is met

## Slide 53: For Loops
High-level code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
add $s0, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:
Notice that the assembly tests for the opposite case (i == 128) than the test in the high-level code (i != 10).

## Slide 54: Less Than Comparisons
High-level code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
addi $s0, $0, 1
addi $t0, $0, 101
loop: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
sll $s0, $s0, 1
j loop
done:
$t1 = 1 if i < 101.

## Slide 55: Arrays
Useful for accessing large amounts of similar data
Array element: accessed by index
Array size: number of elements in the array

## Slide 56: Arrays
5-element array
Base address = 0x12348000 (address of the first array element, array[0])
First step in accessing an array: load base address into a register

## Slide 57: Arrays
// high-level code
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
# MIPS assembly code
# array base address = $s0
lui $s0, 0x1234 # put 0x1234 in upper half of $S0
ori $s0, $s0, 0x8000 # put 0x8000 in lower half of $s0
lw $t1, 0($s0) # $t1 = array[0]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 0($s0) # array[0] = $t1
lw $t1, 4($s0) # $t1 = array[1]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 4($s0) # array[1] = $t1

## Slide 58: Arrays Using For Loops
// high-level code
int array[1000];
int i;
for (i=0; i < 1000; i = i + 1)
array[i] = array[i] * 8;
# MIPS assembly code
# $s0 = array base address, $s1 = i

## Slide 59: Arrays Using For Loops
# MIPS assembly code
# $s0 = array base address, $s1 = i
# initialization code
lui $s0, 0x23B8 # $s0 = 0x23B80000
ori $s0, $s0, 0xF000 # $s0 = 0x23B8F000
addi $s1, $0, 0 # i = 0
addi $t2, $0, 1000 # $t2 = 1000
loop:
slt $t0, $s1, $t2 # i < 1000?
beq $t0, $0, done # if not then done
sll $t0, $s1, 2 # $t0 = i * 4 (byte offset)
add $t0, $t0, $s0 # address of array[i]
lw $t1, 0($t0) # $t1 = array[i]
sll $t1, $t1, 3 # $t1 = array[i] * 8
sw $t1, 0($t0) # array[i] = array[i] * 8
addi $s1, $s1, 1 # i = i + 1
j loop # repeat
done:

## Slide 60: ASCII Codes
American Standard Code for Information Interchange
  assigns each text character a unique byte value
For example, S = 0x53, a = 0x61, A = 0x41
Lower-case and upper-case letters differ by 0x20 (32).

## Slide 61: Cast of Characters