## Slide 1: MIPS Assembly

## Slide 2: A General-Purpose Computer
  Most of today’s computers based on the model proposed by John von Neumann in the late 1940s
  Its major components are:
Central
Processing Unit
Central Processing Unit (CPU): Fetches, interprets, and executes a specified set of operations called Instructions.
Main
Memory
Memory: storage of N words of W bits each, where W is a fixed architectural parameter, and N can be expanded to meet needs.
Input/
Output
I/O: Devices for communicating with the outside world.

## Slide 3: Instructions and Programs
What are instructions?
  the words of a computer’s language
Instruction Set
  the full vocabulary
Stored Program Concept
  The idea that instructions and data of many types can be stored in memory as numbers, leading to the stored program computer

## Slide 4: Processor Architectures
The architecture of a processor chip is a description of its basic components and of its basic operations.
Each processor family has its own architecture.
Assembly language is a programming view of the architecture of a particular processor.
Each type of processor has its own assembly language.
The MIPS architecture is modern and well-designed.
The MIPS chip was designed from the ground up in 1985

## Slide 5: An Assembly Language
An assembly language program describes exactly what the hardware should do, step by step, in terms of the basic operations of the hardware.
In a high level programming language like C or Java a programmer is mostly unaware of computer architecture

## Slide 6: Machine Cycle and Machine Instruction
Most processors endlessly repeat three basic steps. Each machine cycle results in the execution of one machine instruction. A modern processor performs millions of machine cycles per second.
A machine instruction is a pattern of bits that corresponds to a fundamental operation of the processor such as adding two 32-bit integers together or testing if a value is zero. The details of the machine cycle differ between processor families. The machine cycle of most processor chips looks like the following:
Fetch the Instruction. The instruction is fetched from memory. The program counter (PC) is part of the processor. It contains the address of the instruction in memory.
Increment the Program Counter. The program counter now points to the next instruction.
Decode & Execute the Instruction. The operation asked for by the current machine instruction is performed.

## Slide 7
Fetch the Instruction. The instruction is fetched from memory. The program counter (PC) is part of the processor. It contains the address of the instruction in memory.
Increment the Program Counter. The program counter now points to the next instruction
Decode Instruction
Execute the Instruction. The operation asked for by the current machine instruction is performed.
On a 32-bit processor, memory addresses are 32 bits wide and so the program counter (PC) holds a 32 bit address.
Instructions are normally executed in sequence. The program counter advances forward through memory one instruction at a time. Each time an instruction is executed, the next one is automatically selected for the next execution cycle.

## Slide 8: Machine Instructions
Operations like "add two integers" and "compare two integers" are operations that a processor does in one machine cycle.
A machine instruction is a pattern of bits that directs the processor to perform one machine operation.
Here is the machine instruction that directs the MIPS processor to add two 32-bit registers together (a register is a part of the processor that holds a bit pattern).
  0000 0001 0010 1011 1000 0000 0010 0000

## Slide 9: Assembly Language Statement
The layout of a machine instruction is part of the architecture of a processor chip.
Without knowing the layout you can't tell what the instruction means. Even if you know the layout, it is hard to remember what the patterns mean and hard to write machine instructions.
A statement in pure assembly language corresponds to one machine instruction.
Assembly language is much easier to write than machine language.
The previous machine instruction and the assembly language that it corresponds to:
machine instruction assembly language statement
0000 0001 0010 1011 1000 0000 0010 0000 add $t0,$t1,$t2

## Slide 10
The instruction means:
add the integers in registers $t1 and $t2 and
put the result in register $t0.
To create the machine instruction from the assembly language statement a translation program called an assembler is used.
Assembly language much easier to use than machine language for many reasons.
It is hard for humans to keep track of those ones and zeros.
By using symbols programmers gain flexibility in describing the computation.
Assembly language is a compact notation.
Enhanced assembly language includes additional convenience features. It has instructions (called pseudoinstructions) that correspond to several machine instructions.
machine instruction assembly language statement
0000 0001 0010 1011 1000 0000 0010 0000 add $t0,$t1,$t2

## Slide 11: Program Translation
The assembly language statement says the same thing as the machine language instruction, but must be translated into a bit pattern before it can be executed.
An assembly language program consists of assembly language statements, statements that define data, and some additional information that helps in the translation.
Here is a fragment of an assembly language program and its translation into bit patterns.
machine instructions assembly statements
0011 0100 0000 0001 0000 0000 0000 1001 ori $1, $0, 9
0000 0000 0100 0001 0000 0000 0001 1000 mult $2, $1
0011 0100 0000 0001 0000 0000 0000 1001 ori $1, $0, 5
0000 0000 0100 0000 0000 0000 0100 1000 div $8, $1

## Slide 12
An instruction is a primitive operation
  Instructions specify an operation and its operands (the necessary variables to perform the operation)
  Types of operands: immediate, source, and destination
add $t0, $t1, $t2
addi $t0, $t1, 1
Operation
Operands (variables, arguments, etc.)
Source Operands
Destination Operand
Immediate Operand

## Slide 13: Meaning of an Instruction
Operations are abbreviated into opcodes (1-4 letters)
Instructions are specified with a very regular syntax
  First an opcode followed by arguments
  Usually (but not always) the destination is next, then source
  Why this order? Arbitrary…
    … but analogous to high-level language like Java or C
add $t0, $t1, $t2
int t0, t1, t2
t0 = t1 + t2
implies

## Slide 14: Exectution of Instruction
Instruction sequence
  Instructions are executed sequentially from a list …
    … unless some special instructions alter this flow
  Instructions execute one after another
    therefore, results of all previous instructions have been computed
$t0: 0
$t1: 6
$t2: 8
$t3: 10
Variables
add $t0, $t1, $t1
add $t0, $t0, $t0
add $t0, $t0, $t0
sub $t1, $t0, $t1
Instructions
12
24
48
42
What is this program doing?

## Slide 15: The von Neumann model (The Stored-Program Computer)
  Instructions and Data stored in a common memory (“main memory”)
  Sequential semantics: All instructions execute sequentially (or at least appear sequential to the programmer)
Key idea: Memory holds not only data, but coded instructions that make up a program.
Central
Processing Unit
Main Memory
instruction
instruction
instruction
data
data
data
CPU fetches and executes instructions from memory ...
  The CPU is a H/W interpreter
  Program IS simply data for this interpreter
  Main memory: Single expandable resource pool - constrains both data and program size - don’t need to make separate decisions of how large of a program or data memory to buy

## Slide 16
Control Unit
Data
Path
registers
MEMORY
control
status
instructions
data
PC
1101000111011
• INSTRUCTIONS coded in binary
• PROGRAM COUNTER or PC: Address of next instruction to be executed
• Control Unit has circuitry inside to translate instructions into control signals for data path
+1
R1 R2+R3
address
address
“Register File”
Register 0
Register 1
Register 31
a von Neumann Computer

## Slide 17: MIPS Programming Model a representative simple RISC machine
Processor State (inside the CPU)
Main Memory
Fetch/Execute loop:
fetch Mem[PC]
PC = PC + 4†
execute fetched instruction (may change PC!)
repeat!
†MIPS uses byte memory addresses. However, each instruction is 32-bits wide, and *must* be aligned on a multiple of 4 (word) address. Each word contains four 8-bit bytes. Addresses of consecutive instructions (words) differ by 4.
00
PC
r0
r1
r2
...
r31
000000....0
32 bit “words”
0
1
2
3
(4 bytes)
32 bit “words”
0
31
next instruction
General Registers:
A small scratchpad of frequently used or temporary variables
In Comp 411 we’ll use a clean and sufficient subset of the
MIPS-32 core Instruction set.
0 4
8
16 20
Addresses

## Slide 18: MIPS Memory
Memory locations are 32 bits wide
  BUT, they are addressable in different-sized chunks
  8-bit chunks (bytes)
  16-bit chunks (shorts)
  32-bit chunks (words)
  64-bit chunks (longs/double)
We also frequently need access to individual bits! (Instructions help w/ this)
Every BYTE has a unique address (MIPS is a byte-addressable machine)
Every instruction is one word
0
1
2
3
4
5
6
7
Addr
0:
4:
8:
12:
8
9
10
12
12
13
14
15
byte3 byte2 byte1 byte0
short2 short0
long0
long8
31 30 29 … … 4 3 2 1 0

## Slide 19: MIPS Registers
There are 32 named registers [$0, $1, …. $31]
The operands of all ALU instructions are registers
  This means to operate on a variables in memory you must:
    Load the value/values from memory into a register
    Perform the instruction
    Store the result back into memory
  Going to and from memory can be expensive
    (4x to 20x slower than operating on a register)
  Net effect: Keep variables in registers as much as possible!
Special purpose and conventions
  2 registers have specific “side-effects”
    (ex: $0 always contains the value ‘0’… )
  4 registers dedicated to specific tasks by convention
  26 available for general use, but constrained by convention

## Slide 20: MIPS Instruction Formats
All MIPS instructions fit into a single 32-bit word
Every instruction includes various “fields”:
  a 6-bit operation or “OPCODE”
    specifies which operation to execute (fewer than 64)
  up to three 5-bit OPERAND fields
    each specifies a register (one of 32) as source/destination
  embedded constants
    also called “literals” or “immediates”
    16-bits, 5-bits or 26-bits long
    sometimes treated as signed values, sometimes unsigned
There are three basic instruction formats:
R-type, 3 register operands (2 sources, destination)
I-type, 2 register operands, 16-bit constant
OP
rs
rt
rd
OP
rs
rt
16-bit constant
func
shamt
J-type, no register operands, 26-bit constant
OP
26-bit constant

## Slide 21: MIPS ALU Operations
Sample coded operation: ADD instruction
What we prefer to write: add $10, $11, $9 (“assembly language”)
add rd, rs, rt:
“Add the contents of rs to the contents of rt; store the result in rd”
Reg[rd] = Reg[rs] + Reg[rt]
Similar instructions for other ALU operations:
arithmetic: add, sub, addu, subu
compare: slt, sltu
logical: and, or, xor, nor
shift: sll, srl, sra, sllv, srav, srlv
0
0
0
0
0
0
0
1
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
op = 0x00 dictating an ALU function
rs = 11 Reg[11]
source
rd = 10 Reg[10]
destination
rt = 9 Reg[9]
source
unused fields are set to ‘0’
func = 0x20 dictating an add
References to register contents are prefixed by a “$” to distinguish them from constants or memory addresses
R-type:
The convention with MIPS assembly language is to specify the destination operand first, followed by source operands.

## Slide 22: MIPS ALU Operations with Immediate
addi instruction: adds register contents, signed-constant:
Symbolic version: addi $9, $11, -3
“Add the contents of rs to const; store result in rt”
OP = 0x08, dictating addi
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + sxt(imm)
arithmetic: addi, addiu
compare: slti, sltiu
logical: andi, ori, xori, lui
Similar instructions for other ALU operations:
constant field, indicating -3 as second operand
(sign-extended!)
addi rt, rs, imm:
0
0
1
0
0
0
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
Immediate values are sign-extended for arithmetic and compare operations, but not for logical operations.
I-type:

## Slide 23: Why Built-in Constants? (Immediate)
Where are constants/immediates useful?
  SMALL constants used frequently (50% of operands)
    In a C compiler (gcc) 52% of ALU operations use a constant
    In a circuit simulator (spice) 69% involve constants
    e.g., B = B + 1; C = W & 0x00ff; A = B + 0;
Examples: addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4

## Slide 24: First MIPS Program (fragment)
Suppose you want to compute the expression:
  f = (g + h) – (i + j)
    where variables f, g, h, i, and j are assigned to registers $16, $17, $18, $19, and $20 respectively
    what is the MIPS assembly code?
  Questions to answer:
    How did these variables come to reside in registers?
    Answer: We need more instructions which allow data to be explicitly loaded from memory to registers, and stored from registers to memory
  add $8,$17,$18 # (g + h)
  add $9,$19,$20 # (i + j)
  sub $16,$8,$9 # f = (g + h) – (i + j)

## Slide 25: MIPS Register Usage Conventions
Some MIPS registers assigned to specific uses
  by convention, so programmers can combine code pieces
    will cover the convention later
  $0 is hard-wired to the value 0

## Slide 26
More instructions
  accessing memory
  branches and jumps
  larger constants
  multiply, divide
  etc.