## Slide 1: Processor: Datapath and Control
Single cycle processor
  Datapath and Control
Multicycle processor
  Datapath and Control

## Slide 2: Processor Design
Processor design
  datapath and control unit design
  processor design determines
    clock cycle time
    clock cycles per instruction
Performance of a machine is determined by
  Instruction count
  clock cycle time
  clock cycles per instruction

## Slide 3
How to Design a Processor: step-by-step
1. Analyze instruction set => datapath requirements
  the meaning of each instruction is given by the register transfers
  datapath must include storage element for ISA registers
    possibly more
  datapath must support each register transfer
2. Select set of datapath components and establish clocking methodology
3. Assemble datapath meeting the requirements
4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
5. Assemble the control logic

## Slide 4: Single Cycle Processor
Single cycle processor
  Pros: one clock cycle per instruction
  Cons: too long cycle time, too low clocking frequency
Design a processor
  analyze instruction set (the meaning of each instruction is given by the register transfers)
  timing of each instruction
  datapath support each register transfer
  select datapath components and establish clocking methodology
  analyze implementation of each instruction to determine setting of control points that affect register transfer
  assemble control logic and datapath components

## Slide 5: Clocking Methodology
Edge-triggered clock
setup time
hold time
all storage elements clocked by the same clock
combinational logic block:
  inputs are updated at each clock tick
  all outputs must be stable before the next clock tick

## Slide 6
Clocked Logic Timing

## Slide 7
Timing Analysis, Logic Delay
Worst case CL delay limits T.
What is the smallest T that produces correct operation?

## Slide 8
Flip Flop delays:
D
Q
clk-to-Q ?
CLK == 0
Sense D, but Q
outputs old value.
CLK 0->1
Capture D, pass
value to Q
CLK
setup ?
hold ?
clk-to-Q
setup
hold

## Slide 9
Flip Flops have internal delays
D
Q
CLK
Value of D is sampled on positive clock edge.
D
Q
t_setup
t_clk-to-Q
CLK
Q outputs sampled value for rest of cycle.

## Slide 10
Combinational Logic
ALU “time budget”

## Slide 11
The MIPS Instruction Formats
All MIPS instructions are 32 bits long. The three instruction formats:
  R-type
  I-type
  J-type
The different fields are:
  op: operation of the instruction
  rs, rt, rd: the source and destination register specifiers
  shamt: shift amount
  funct: selects the variant of the operation in the “op” field
  address / immediate: address offset or immediate value
  target address: target address of the jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 12: Register Transfers
add $1, $2, $3; rs = $2, rt = $3, rd = $1
  R[rd] <- R[rs] + R[rt} PC <- PC + 4
sub $1, $2, $3; rs = $2, rt = $3, rd = $1
  R[rd] <- R[rs] - R[rt] PC <- PC + 4
ori $1, $2, 20; rs = $2, rt = $1
  R[rt] <- R[rs] + zero_ext(imm16) PC <- PC + 4
lw $1, 200($2); rs = $2, rt = $1
  R[rt] <- MEM{R[rs] + sign_ext(imm16)} PC <- PC + 4
sw $1, 200($2); rs = $2, rt = $1
  MEM{R[rs] + sign_ext(imm16)} <- R[rt] PC <- PC + 4

## Slide 13: Components
Memory: hold instruction and data
Registers: 32 32-bit registers
  read rs
  read rt
  write rd
  write rt
Program counter
Extender
Add and Sub registers or extended immediates
Add 4 to PC or Add extended immediate to PC (jump inst)

## Slide 14: Combinational Logic Elements
Adder
MUX (multi-plexor)
ALU
32
32
A
B
32
Sum
Carry
32
32
A
B
32
Result
OP
32
A
B
32
Y
32
Select
Adder
MUX
ALU
CarryIn
(to add values)
(to chose between values)
(to do add, subtract, or)

## Slide 15
Storage Element: Register (Basic Building Block)
Register
  Similar to the D Flip Flop except
    N-bit input and output
    Write Enable input
  Write Enable:
    negated (0): Data Out will not change
    asserted (1): Data Out will become Data In
Clk
Data In
Write Enable
N
N
Data Out

## Slide 16: Sequential Logic Elements
Registers: n-bit input and output, D F/F, write enable
rs, rt, rd : register specifiers
registers
read
register1
read
register2
write
register
write
data
read
data1
read
data2

## Slide 17: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory
  updating the PC to hold the address of the next instruction
Read
Address
Instruction
Instruction
Memory
Add
PC
4
  PC is updated every cycle, so it does not need an explicit write control signal
  Instruction Memory is read every cycle, so it doesn’t need an explicit read control signal

## Slide 18
Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  reading two values from the Register File
    Register File addresses are contained in the instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2

## Slide 19
Executing R Format Operations
R format operations (add, sub, slt, and, or)
  perform the (op and funct) operation on values in rs and rt
  store the result back into the Register File (into location rd)
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
  The Register File is not written every cycle (e.g. sw), so we need an explicit write control signal for the Register File

## Slide 20
Executing Load and Store Operations
Load and store operations involves
  compute memory address by adding the base register (read from the Register File during decode) to the 16-bit signed-extended offset field in the instruction
  store value (read from the Register File during decode) written to the Data Memory
  load value, read from the Data Memory, written to the Register File
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
16
32

## Slide 21
Executing Branch Operations
Branch operations involves
  compare the operands read from the Register File during decode for equality (zero ALU output)
  compute the branch target address by adding the updated PC to the 16-bit signed-extended offset field in the instr
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)

## Slide 22
Executing Jump Operations
Jump operation involves
  replace the lower 28 bits of the PC with the lower 26 bits of the fetched instruction shifted left by 2 bits
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
address
26
4
28

## Slide 23
Creating a Single Datapath from the Parts
Assemble the datapath segments and add control lines and multiplexors as needed
Single cycle design – fetch, decode and execute each instructions in one clock cycle
  no datapath resource can be used more than once per instruction, so some must be duplicated (e.g., separate Instruction Memory and Data Memory, several adders)
  multiplexors needed at the input of shared elements with control lines to do the selection
  write signals to control writing to the Register File and Data Memory
Cycle time is determined by length of the longest path

## Slide 24
Fetch, R, and Memory Access Portions
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 25
Adding the Control
Selecting the operations to perform (ALU, Register File and Memory read/write)
Controlling the flow of data (multiplexor inputs)
I-Type:
op
rs
rt
address offset
31
25
20
15
0
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
Observations
  op field always in bits 31-26
  addr of registers
  to be read are always specified by the rs field (bits 25-21) and rt field (bits 20-16); for lw and sw rs is the base register
  addr. of register to be written is in one of two places – in rt (bits 20-16) for lw; in rd (bits 15-11) for R-type instructions
  offset for beq, lw, and sw always in bits 15-0
J-type:
31
25
0
op
target address

## Slide 26
Single Cycle Datapath with Control Unit
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 27
R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 28
Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 29
Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 30
Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 31
Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 32
Adding the Jump Operation
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Shift
left 2
0
1
Jump
32
Instr[25-0]
26
PC+4[31-28]
28

## Slide 33
Single Cycle Control Unit: ALU control
control
unit
Instr[31-26]
ALUOp
ALU
control
to ALU
operation
Instr[5-0]
On page 302, Operation has 4 bits with the first bit always zero
add
sub.
add
sub.
and
or
set
on less
than

## Slide 35
ALU Control Implementation

## Slide 36
On page 301, ALU control lines = Operation
ALU control lines Function
0000 AND
0001 OR
0010 add
0110 subtract
0111 set on less than
1100 NOR

## Slide 37
instruction opcode | ALUOP | Instruction operation | Funct field | Desired ALU action | ALU control input, i.e., Operation
LW | 00 | load word | xxxxxx | add | 0010
SW | 00 | store word | xxxxxx | add | 0010
Branch equal | 01 | branch equal | xxxxxx | subtract | 0110
R type | 10 | add | 100000 | add | 0010
R type | 10 | subtract | 100010 | subtract | 0110
R type | 10 | AND | 100100 | and | 0000
R type | 10 | OR | 100101 | or | 0001
R type | 10 | set on less than | 101010 | set on less than | 0111

## Slide 38
Setting of the control signals
Instru-ction | RegDst | ALUSrc | Memto Reg | Reg Write | Mem Read | Mem Write | Branch | ALU Op1 | ALU Op0
R type | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw | x | 1 | x | 0 | 0 | 1 | 0 | 0 | 0
beq | x | 0 | x | 0 | 0 | 0 | 1 | 0 | 1

## Slide 40
Control Unit PLA Implementation